## Slide 1
COMPASS SCENARIO DATABASE · DISSERTATION PAPER 1
High renewables or engineered carbon management?
Century-long wellbeing implications across global IAM pathways
World results first. R10 regions explain the pattern. Transparent diagnostics define the limits.
Final analysis · primary classification excludes land-based CDR

## Slide 2
THE PAPER IN ONE VIEW
EXECUTIVE SUMMARY
Three conclusions, with different evidentiary strength
COMPASS Scenario Database · Paper 1 · 2020–2100
02
1 · JOBS
High-RE is higher
Across the full ensemble, High-RE has substantially more modeled renewable electricity job-years at both ambition levels.
2 · ENERGY DEPRIVATION
High-RE is generally lower
The full database shows lower modeled energy gap and deprivation headcount. SCI 2°C results are heterogeneous.
3 · MORTALITY
No universal winner
The reporting-complete PM2.5 diagnostic is useful, but coverage and composition prevent a headline portfolio ranking.

## Slide 3
RESEARCH QUESTION
DESIGN
The comparison is deliberately two-part
COMPASS Scenario Database · Paper 1 · 2020–2100
03
WELLBEING QUESTION
Across World and R10 regions, what differs between renewable-intensive and engineered-carbon-management-intensive pathways at the same climate ambition?
DIAGNOSTIC QUESTION
Are pooled contrasts carried by a particular IAM composition, regional pattern, or reporting subset?
Every pathway is compared within its ambition cell
1.5°C and 2°C are never pooled. Full-database results describe the ensemble; SCI-vetted results are reported separately. Within-model contrasts test whether composition is driving the pooled pattern.

## Slide 4
CLASSIFICATION
PORTFOLIO IDENTITY
The primary contrast is RE versus engineered CMT—not “all removals”
COMPASS Scenario Database · Paper 1 · 2020–2100
04
Arm
Focal deployment
Exclusion rule
Why
High-RE
Top tercile: renewable capacity
Engineered CMT not top tercile
Identifies RE-led portfolios
High engineered-CMT
Top tercile: novel CDR + fossil/industrial CCS
Renewables not top tercile
Identifies engineered-management portfolios
Land CDR
Excluded from primary axis
Retained for “all-removals” sensitivity
Keeps the energy-system motivation distinct
Classification uses cumulative 2020–2100 deployment, so labels describe long-run portfolios rather than a single benchmark year.
Sensitivity analyses retain the strict polar rule and the total-CDR (all-removals) question; neither substitutes for the primary engineered-CMT contrast.

## Slide 5
SAMPLE COVERAGE
TRANSPARENCY
The final full-database contrast is larger than the earlier total-CDR sample
COMPASS Scenario Database · Paper 1 · 2020–2100
05
Sample / ambition
High-RE
High engineered-CMT
Comparison count
Full · 1.5°C
64
64
128
Full · 2°C
239
239
478
SCI · 1.5°C
7
7
14
SCI · 2°C
63
63
126
SCI 1.5°C is intentionally small
24 candidates → 22 classifiable → 7 pathways per arm. Two candidates lack the classification metrics; eight fall outside the paired arms.
New engineered-CMT primary classification: 606 selected full-database pathways and 140 SCI-vetted pathways. Earlier deck: 579 and 106 under total CDR.

## Slide 6
PART 1
Methodology
Scenario outputs are translated into bounded wellbeing-relevant indicators.

## Slide 7
METHODOLOGY · ELECTRICITY EMPLOYMENT
OUTCOME 1
Capacity deployment becomes gross/direct electricity job-years
COMPASS Scenario Database · Paper 1 · 2020–2100
07
Stage
Input / operation
Meaning
IAM output
R10 technology-specific capacity additions and operating capacity
The deployment pathway
Post-processing
Published manufacturing, construction, installation, and O&M employment factors
Job-years by technology
Outcome
Renewable electricity job-years per 1,000 people
Not net economy-wide employment or job quality
Mechanism: wind and solar generally require more distributed manufacturing, construction, installation, and operations activity per unit of capacity.
MECHANICAL WHY
High-RE portfolios build more RE capacity; CMT investment shifts more system effort to removal, capture, storage, and fuel supply.
POLICY WHY
Domestic content, workforce programs, grid build-out, and trade determine whether modeled activity becomes local employment.

## Slide 8
METHODOLOGY · ENERGY DEPRIVATION
OUTCOMES 2–3
Final energy availability becomes two modeled decent-living indicators
COMPASS Scenario Database · Paper 1 · 2020–2100
08
Indicator
IAM input
Post-processing / interpretation
Energy gap (GJ/cap)
Regional final energy and population
Energy needed to lift people below a regional decent-living threshold
Headcount (%)
Regional final energy per person
Threshold + lognormal within-region distribution + inequality parameter
These are distributional final-energy-deprivation proxies—not observed household access, consumption surveys, or income poverty.
MECHANICAL WHY
RE-intensive pathways often co-occur with electrification and higher final-energy availability relative to the threshold.
POLICY WHY
Grid access, affordability, reliability, appliances, and tariff design decide whether supply reaches people.

## Slide 9
METHODOLOGY · MORTALITY
OUTCOME 4
PM2.5 mortality is a reporting-complete, coverage-qualified diagnostic
COMPASS Scenario Database · Paper 1 · 2020–2100
09
Stage
Decision
Reason
Emission inputs
Direct R10 SO₂, NOₓ, BC, OM, NH₃ only
No World-to-R10 allocation; no external NH₃ sidecar
Air-quality response
TM5-FASST → PM2.5 exposure → FUSION mortality response
Consistent, fast scenario post-processing
Coverage rule
Only complete precursor records enter final comparison
Reject rather than fill structurally missing pathways
422 valid PM2.5 outputs from 643 classified targets; 150 incomplete records rejected. Short interior interpolation was permitted, but no values were interpolated.
Interpretation: PM2.5-attributable mortality only, not total air-pollution mortality—and not a universal High-RE vs High-CMT rank.

## Slide 10
METHODS LOGIC
MECHANISM
The path from scenario portfolio to wellbeing outcome is explicit
COMPASS Scenario Database · Paper 1 · 2020–2100
10
Technology portfolio
IAM pathway
Physical output
R10 variables
→
Post-processing
Outcome model
→
Interpretation
Wellbeing
JOBS
Capacity × employment factors
ENERGY DEPRIVATION
Final energy × threshold + distribution
MORTALITY
Precursors × TM5-FASST × FUSION

## Slide 11
PART 2
Results
World results provide the takeaway. R10 results show why it appears.

## Slide 12
RESULTS · WORLD
WORLD · PRIMARY
Full database: High-RE is higher on jobs and lower on modeled energy deprivation
COMPASS Scenario Database · Paper 1 · 2020–2100
12
Outcome (High-RE − High engineered-CMT)
1.5°C
2°C
Direction
RE job-years per 1,000 people
+396 (687 vs 291)
+288 (461 vs 173)
High-RE higher
Energy gap, GJ/cap
−5.7 (13.0 vs 18.7)
−4.5 (11.1 vs 15.5)
High-RE lower
Deprivation headcount, pp
−2.25 (4.61 vs 6.86)
−1.77 (4.02 vs 5.80)
High-RE lower
The two ambitions differ in scale—not in the full-database direction for the three non-mortality outcomes.
1.5°C jobs
+396
2°C jobs
+288
1.5°C energy gap
−5.7 GJ/cap
2°C energy gap
−4.5 GJ/cap

## Slide 13
RESULTS · WORLD
WORLD · SCI
SCI-vetted evidence confirms the jobs contrast; 2°C deprivation is not uniform
COMPASS Scenario Database · Paper 1 · 2020–2100
13
Outcome (High-RE − High engineered-CMT)
SCI 1.5°C
SCI 2°C
Reading
RE job-years per 1,000 people
+262 (526 vs 264)
+111 (293 vs 182)
Jobs remain higher
Energy gap, GJ/cap
−2.4 (18.4 vs 20.8)
+1.5 (20.5 vs 19.0)
2°C reverses
Deprivation headcount, pp
−0.99 (6.86 vs 7.85)
+0.73 (7.60 vs 6.87)
2°C reverses
The SCI sample is a different evidence set—not a “cleaner” version of the full ensemble. Report the divergence rather than averaging it away.
SCI sample sizes: 7 vs 7 at 1.5°C; 63 vs 63 at 2°C.

## Slide 14
RESULTS · MORTALITY
WORLD · DIAGNOSTIC
The reporting-complete PM2.5 diagnostic has no stable pooled portfolio winner
COMPASS Scenario Database · Paper 1 · 2020–2100
14
Sample
1.5°C: RE − CMT, million deaths
2°C: RE − CMT, million deaths
Interpretation
Full database
−8.69
+3.03
Pooled direction changes
SCI-vetted
−50.42
+22.45
Pooled direction changes
WHAT IS STABLE
At 2°C, matched within-model full-database comparisons all point toward lower High-RE mortality, but only three models qualify.
WHAT IS NOT STABLE
Coverage differs by arm and model family; pooled medians change with sample composition. The paper should not rank portfolios on mortality.
Coverage is reported with every mortality result: e.g., full 1.5°C 42/64 CMT vs 37/64 RE; full 2°C 138/239 vs 168/239.

## Slide 15
RESULTS · INTERPRETATION
DIAGNOSTIC
The mortality caveat is a result about evidence quality—not a weakness to hide
COMPASS Scenario Database · Paper 1 · 2020–2100
15
COVERAGE
Missing precursor reporting is structural
Scenarios that lack a required pollutant cannot support a comparable PM2.5 mortality estimate.
COMPOSITION
Pooled arms contain different IAM mixtures
A pooled median can move even when the qualifying within-model comparison has a different direction.
BOUNDED CLAIM
Mortality is a QA check
It tests whether air-quality implications are plausible under complete reporting; it does not establish a global ranking.
This is why the paper leads with jobs and energy deprivation, then shows mortality transparently as a qualified diagnostic.

## Slide 16
PART 3
Regional diagnosis
World results are aggregation outcomes: regions differ in stakes, scale, and mechanisms.

## Slide 17
RESULTS · R10 JOBS
R10 · PRIMARY
High-RE produces more modeled RE job-years in almost every region
COMPASS Scenario Database · Paper 1 · 2020–2100
17
Region
1.5°C RE − CMT
2°C RE − CMT
Signal
Africa
+832
+538
largest positive
India+
+733
+455
large positive
Rest of Asia
+666
+442
large positive
Middle East
+557
+411
large positive
Latin America
+221
+194
positive
China+
+124
+91
positive
North America
+154
+103
positive
Europe
+63
+58
positive
Exceptions are small
Pacific OECD is near zero or modestly positive; no R10 region reverses the strong global jobs result in both ambitions.
Values are High-RE − High engineered-CMT renewable job-years per 1,000 people; they quantify modeled sectoral activity, not labour-market welfare.

## Slide 18
RESULTS · R10 ENERGY DEPRIVATION
R10 · PRIMARY
The World deprivation result is driven by high-stakes regions—but it is not universal
COMPASS Scenario Database · Paper 1 · 2020–2100
18
Region
Energy gap difference: 1.5°C / 2°C
Headcount difference: 1.5°C / 2°C
Reading
Africa
−22.1 / −24.8 GJ/cap
−10.0 / −9.5 pp
largest improvement
Latin America
−23.1 / −11.4 GJ/cap
−7.6 / −3.4 pp
large improvement
India+
−0.6 / −0.7 GJ/cap
−0.5 / −0.7 pp
modest improvement
Rest of Asia
−2.3 / +3.0 GJ/cap
−0.9 / +1.0 pp
ambition-dependent
Middle East / North America
positive gaps
positive headcounts
reversal
Negative values favor High-RE. The regional pattern makes the World average interpretable: high baseline shortfalls magnify changes in final energy availability.

## Slide 19
RESULTS · REGIONAL MORTALITY
R10 · DIAGNOSTIC
Read PM2.5 mortality only where the precursor-reporting comparison is complete
COMPASS Scenario Database · Paper 1 · 2020–2100
19
WHERE WORLD TOTALS COME FROM
Large populations and high baseline pollution make South and East Asian regions central to absolute PM2.5 mortality totals.
WHY REGIONAL DIRECTION DIFFERS
Coal, industry, transport, biomass, agricultural NH₃, and the pace of end-use electrification vary across R10 regions.
Do not convert incomplete reporting into a regional causal story
A regional contrast is reported only when both pathway arms contain complete direct R10 precursor emissions and comparable models. This prevents a “clean-looking” map from hiding missing NH₃ or other precursors.

## Slide 20
REGIONAL DIAGNOSIS
SYNTHESIS
Which regions mechanically drive the World story?
COMPASS Scenario Database · Paper 1 · 2020–2100
20
SCALE
China+, India+, Rest of Asia
Large deployment volumes and population mean these regions can dominate world job-years and PM2.5 totals.
STAKES
Africa, India+, Latin America
High starting energy shortfalls mean a change in final energy availability moves the deprivation indicators most.
DIVERGENCE
Middle East, North America, Pacific OECD
Fossil-asset structure, trade, resource quality, and modelled energy demand can produce different deprivation patterns.
World is not a vote count across R10 regions: it is a population-, energy-, and deployment-weighted aggregation.

## Slide 21
PART 4
Why the patterns arise
The results describe scenario portfolios; the mechanism is technological, distributional, and policy-mediated.

## Slide 22
MECHANISMS
WHY · JOBS
Why the job-years result is mechanically plausible
COMPASS Scenario Database · Paper 1 · 2020–2100
22
Portfolio feature
System consequence
Wellbeing-relevant implication
High-RE
More wind/solar additions and operating capacity
More modeled manufacturing, construction, installation, and O&M job-years
High engineered-CMT
More capture/removal/storage and remaining fuel-system activity
Less RE-build activity per person—without implying fewer total economy jobs
Regional context
Supply chains, labour intensity, import dependence
Modeled job activity need not equal domestic job quality or inclusion
Real-world policy bridge: renewable targets alone are not a workforce strategy. Grid planning, training, local-content rules, labour standards, and just-transition policy determine who benefits.

## Slide 23
MECHANISMS
WHY · ENERGY
Why deprivation can improve—and can reverse—by region
COMPASS Scenario Database · Paper 1 · 2020–2100
23
MECHANICAL PATHWAY
Technology portfolios co-vary with electrification, efficiency, fuel switching, and final energy availability. The DLE model translates those changes relative to a regional threshold.
WHY AFRICA AND LATIN AMERICA MATTER
A given change in available final energy can reduce a large shortfall or affect a large population below the threshold.
WHY REVERSALS ARE CREDIBLE
CMT-intensive scenarios can still deploy substantial renewables; demand, end-use allocation, model structure, and trade can outweigh the portfolio label in a region.
POLICY BRIDGE
Affordable connections, reliability, productive-use demand, appliance efficiency, and tariff design are the missing links between energy supply and household wellbeing.

## Slide 24
MECHANISMS · MORTALITY
WHY · AIR QUALITY
Why High-RE and High engineered-CMT can look similar on PM2.5
COMPASS Scenario Database · Paper 1 · 2020–2100
24
Both pathways meet the same temperature target; “High engineered-CMT” does not mean “high fossil pollution.”
Reason
How it affects the comparison
Shared mitigation
1.5°C and 2°C CMT scenarios still reduce fossil combustion and deploy renewables, so both can receive large pollution-health benefits.
Non-power sources
Industry, transport, biomass, agriculture, and NH₃ drive PM2.5 too; a power-sector portfolio label cannot isolate all precursors.
Evidence constraint
Complete emissions reporting differs across model families and pathway arms, shifting pooled medians.
Policy implication: achieving the climate target is necessary for cleaner air, but the co-benefit depends on which emitting sectors are transformed and how completely emissions are reported.

## Slide 25
DIAGNOSTIC EVIDENCE
ROBUSTNESS
Model composition is a core result, not an appendix footnote
COMPASS Scenario Database · Paper 1 · 2020–2100
25
Pooled ensemble
Describes the set of scenarios observed in the database. It can mix different IAM families across the two portfolio arms, especially after requiring outcome coverage.
Within-model comparison
Keeps an IAM only when it supplies both pathway arms in the same ambition-region cell. It is the better test of whether the pooled contrast is model-composition dependent.
Use association language for pooled results. Treat agreement between pooled and within-model evidence as stronger support; show disagreement as diagnosis.

## Slide 26
ROBUSTNESS
ROBUSTNESS
The primary result is distinguished from related sensitivity questions
COMPASS Scenario Database · Paper 1 · 2020–2100
26
Specification
What it tests
Role in paper
Primary: engineered-CMT, broad paired top-tercile rule
Energy-system contrast: High-RE vs novel CDR + fossil/industrial CCS
Main findings
Strict polar portfolios
Whether technology extremes sharpen or alter the contrast
Sensitivity
Total CDR / all removals
Whether land removals change the interpretation
Supplement: different substantive question
Mortality reporting-complete screen
Whether PM2.5 conclusions survive complete direct R10 inputs
QA diagnostic
Robustness does not mean forcing every outcome to agree. It means specifying which comparison each statistic can credibly answer.

## Slide 27
PAPER CONTRIBUTION
CONTRIBUTION
A precise and dissertation-ready claim set
COMPASS Scenario Database · Paper 1 · 2020–2100
27
The paper can credibly claim that:
1
Within the full global IAM ensemble, High-RE pathways are associated with substantially more modeled RE job-years and generally lower modeled energy deprivation than High engineered-CMT pathways.
2
R10 heterogeneity explains the World patterns: high-stakes deprivation regions and high-scale deployment regions matter more than a region-count average.
3
PM2.5 mortality is informative only after reporting-complete screening and remains non-rankable across all samples and ambitions—an evidence-quality result with substantive value.

## Slide 28
BOTTOM LINE
High-RE pathways carry the clearer wellbeing advantage where the evidence is strongest.
They are associated with more renewable-electricity job-years and—across the full ensemble—less modeled energy deprivation. Regional diagnosis makes that global result interpretable; transparent mortality coverage keeps the claim honest.
The paper’s contribution is not a universal technology winner. It is a transparent map of where pathway portfolios matter for wellbeing—and where the database cannot yet answer.